| Equipment/Environment | User Visual Inspections | Formal Visual Inspections | Combined Inspection & Testing |
| --- | --- | --- | --- |
| Battery operated (less than 20 volts) | No | No | No |
| Extra low voltage (less than 50 volts AC) e.g. telephone and low voltage desk lights | No | No | No |
| Information technology e.g. display screen equipment (DSE) | No | Yes, 2 – 4 years | No, if double insulated otherwise up to 5 years |
| Photocopiers, fax machines not hand held, rarely moved | No | Yes, 2 – 4 years | No, if double insulated otherwise up to 5 years |
| Double insulated equipment: not hand held. Moved occasionally e.g. fans, table lamps, slide and overhead projectors | No | Yes, 2 – 4 years | No |
| Double insulated equipment: hand held e.g. some floor cleaners | Yes | Yes, 6 months – 1 year | No |
| Earth equipment (Class 1): e.g. electric kettles, some floor cleaners | Yes | Yes, 6 months – 1 year | Yes, 1 – 2 years |
| Cables, (leads) and plugs, connected to the above appliances, extension leads connected to mains voltage | Yes | Yes, 6 months – 4 years depending on the type of equipment it is connected to | Yes, 1 – 5 years depending on the type of equipment it is connected to |

Recommended test periods for portable electrical equipment

The procedure for inspection and testing of electrical equipment, indicated in the above tables, incorporates the recommendations contained in the Installation of Electrical Engineers (IEE) Regulations and also reflect good practice throughout industry.